## Slide 1: The Use of Loaded Antennas as Scattering Relays for Post-Cellular Networks with Closely Spaced Terminals
Intermediate Presentation, Bernhard Gahr
Supervisor: Yahia Hassan
Professor: Armin Wittneben

## Slide 2: Outline
Motivation
System Setup
Receiver - Overview
Impact of Coupling
Analysis of Interference
Cost Function
Gradient Search
Simulation Results
Outlook

## Slide 3: Motivation/Problem Description
Future systems are expected to be characterized by
  Very high density of nodes (e.g. sensor networks, coverage in stadium)
  Large number of antennas
  Lower frequencies
This leads to closely spaced antennas that are coupled
One of the most crucial bottlenecks is the interference
Idea is to improve achievable rates by using only passive relays and matching networks
Coupling between the relays and the receivers is used to minimize the interference.
Approach of improving the rates is gradient search.

## Slide 4: System Setup
No Coupling between the transmitters
Coupling between the relays and the receivers
Passive relays
  Relays interact only by their coupling
Connection pairs
  Rx1 and Tx1
  Rx2 and Tx2

## Slide 5: Receiver - Schematic
Coupling matrix Zc
Open circuit voltages Vo at the antennae
Uncoupled matching network ZM
Low-noise Amplifier
Further circuitry represented by RL
Passive relays represented by pure imaginary XRel
4 Noise sources, in the following only one considered

## Slide 6: Uncoupled Matching
Each antenna has its own matching network
No connection between the matching networks
For antenna the matching network is
Simplest way of representation is using the T network:

## Slide 7: Receiver - Impact of Coupling
Find an equivalent circuit, with only the required branches
V’0 contains the signal at the antenna and the Signal from the coupling
ZC’ is affected by the equivalent input impedances of the other receivers and the Antennae loads

## Slide 8: Receiver - Transfer Function
HL,0’
HM,0’
HLNA,M
HL,LNA
Transfer the open circuit voltages to parallel input voltages
The remaining transfer functions (HL,LNA and HLNA,M) are independent of XRel.

## Slide 9: Receiver - Interference
To cancel the interference it is sufficient to look at the coupling transfer function (c.f. 6) and the spatial channel from the interferer
,and
As every later transfer function is applied as well to the signal part as to the interference part, an interference free connection is only achieved, if the following property holds

## Slide 10: Receiver - Interference
To cancel the interference it is sufficient to look at the coupling transfer function (c.f. 6) and the spatial channel from the interferer
,and
As every later transfer function is applied as well to the signal part as to the interference part, an interference free connection is only achieved, if the following property holds

## Slide 11: Cost Functions
User rate for user i:
Lp-Norm, in the following we look at the sum rate (p=1)
In the following, we try to maximize the cost function by gradient search

## Slide 12: Behavior of the Function
We consider only two relays
We evaluate the sum rate
against different load values
at different input power
<Clip,Seed94>

## Slide 13: Behavior of the Function
Difficulties in finding the global maximum due to
Non convex problem
Optimal value shifts for different input power
Large performance difference between local optimas

## Slide 14: Gradient Search Optimization - Optimum Shifts
Difficulties in finding the global maximum due to
Non convex problem
Optimal value shifts for different input power
Large performance difference between local optimas

## Slide 15: Behavior of the Function
Difficulties in finding the global maximum due to
Non convex problem
Optimal value shifts for different input power
Large performance difference between local optimas

## Slide 16: Gradient Search Optimization - Optimum Shifts
Up to 30dB: optimizing only one of the connection pair and eliminating the other leads to a better performance.
Over 30dB: gradient search runs into a local maximum - only for high SNR, the second connection is enabled.

## Slide 17: Gradient Search Optimization - Local Optimas

## Slide 18: Optimization
For the gradient search, the analytical gradient was derived
The constraints we have are
  The relays are pure imaginary
  The submatrices of the matching network must be diagonal and pure imaginary
An adaptive step size is used for faster convergence
For correctness it was compared to
The numerical gradient
The existing method from Yahia for a point to point MIMO
The built-in function fminunc

## Slide 19: Gradient Search Optimization - Convergence
Sum rate vs gradient iteration steps
Even after 500 iterations, we may have an abrupt change in the sum rate

## Slide 20: Simulation Settings
For the simulations, the following settings were used
No. of Relays: 4
No. of Tx: 2
No. of Tx antennae: 1
No. of Rx: 2
No. of Rx antennae: 1
Lp-Norm: 1
Gradient Iteration: 1500

## Slide 21: Simulation Results
Empirical CDF-Plots at different SNRs for 4030 channel realizations

## Slide 22: Simulation Results
Empirical CDF-Plots at different SNRs for XX channel realizations for only two relays

## Slide 23: Outlook
Simulations with
Larger number of transmit and receive antennae
Different receiver structures (LMMSE)
Larger number of relays
Larger number of connection pairs
Different precoding matrices at the transmitters

## Slide 24: Gradient Search Optimization - Performance